## Slide 1
TDMA Schedule Optimizer and EMANE Integration
Distance-2 graph colouring for collision-free slot planning, enforced in an EMANE emulation
Hardik Katariya
Vaan Megam Networks internship task | 5 October 2026
Notes: Part 1 is the mandatory scheduler and Part 2 is the EMANE integration. Tags on each slide mean: [run] observed on this machine, [from docs, not run] reasoning or documentation only.

## Slide 2
The problem
2
TDMA Schedule Optimizer and EMANE Integration
[from docs, not run]
• 16 radios, one frequency, taking turns in fixed time slots.
• Close radios interfere, far radios can reuse the same slot.
• Goal: assign a slot per radio with no receiver collisions, using as few slots as possible.
• Two collision cases: direct link (distance 1) and hidden terminal (distance 2).
Direct link (distance 1)
A and B are neighbours. They must use different slots.
Hidden terminal (distance 2)
A and C cannot hear each other but both reach B. They collide at B, so they need different slots.
Notes: Restates the brief.

## Slide 3
Approach
3
TDMA Schedule Optimizer and EMANE Integration
[from docs, not run]
Hidden terminal: A and C are 2 hops apart
A
B
C
G squared joins A and C with an edge, so they get different colours.
Nodes more than 2 hops apart have no edge, so they may share a colour.
• Model radios as a unit-disk graph G: edge when within 500 m.
• Collision-free schedule = proper colouring of the distance-2 conflict graph G squared.
• Each colour is one slot. Non-adjacent nodes reuse slots, which is spatial reuse.
• Centralized Python brain plans it, EMANE enforces it.
Notes: Two transmitters conflict when they are neighbours or share a neighbour. That is G squared. A proper colouring of G squared is a collision-free schedule and each colour is one slot.

## Slide 4
The algorithm
4
TDMA Schedule Optimizer and EMANE Integration
Minimum slots = chromatic number of G squared, which is NP-hard. [from docs, not run]
Three layers in the code [run]
1 Upper bound
Five NetworkX greedy strategies plus 300 randomized DSATUR restarts.
2 Lower bound
Max clique in G squared. Every node in a clique needs its own slot.
3 Exact search
colour_with_k tries one slot fewer. On the sample the heuristic already met the lower bound, so it was not needed there.
Report a lower bound, an upper bound and "optimal" only when they meet.
Notes: Minimum slots is the chromatic number, which is NP-hard, so the solver brackets the answer with bounds. On the sample the heuristic already met the lower bound, so the exact search was not needed there.

## Slide 5
Part 1 results
5
TDMA Schedule Optimizer and EMANE Integration
[run]
Slot \ Node | 01 | 02 | 03 | 04 | 05 | 06 | 07 | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Slot 00 | 1 | · | · | 1 | · | · | · | · | · | · | · | · | 1 | · | · | 1
Slot 01 | · | 1 | · | · | · | · | · | · | · | · | · | · | · | 1 | · | ·
Slot 02 | · | · | 1 | · | · | · | · | · | · | · | · | · | · | · | 1 | ·
Slot 03 | · | · | · | · | 1 | · | · | 1 | · | · | · | · | · | · | · | ·
Slot 04 | · | · | · | · | · | 1 | · | · | · | · | · | · | · | · | · | ·
Slot 05 | · | · | · | · | · | · | 1 | · | · | · | · | · | · | · | · | ·
Slot 06 | · | · | · | · | · | · | · | · | 1 | · | · | 1 | · | · | · | ·
Slot 07 | · | · | · | · | · | · | · | · | · | 1 | · | · | · | · | · | ·
Slot 08 | · | · | · | · | · | · | · | · | · | · | 1 | · | · | · | · | ·
Node to slot (node:slot) 01:0 02:1 03:2 04:0 05:3 06:4 07:5 08:3 09:6 10:7 11:8 12:6 13:0 14:1 15:2 16:0
• 16 nodes, 42 links, 500 m range.
• 9-slot frame, lower bound 9, proven optimal for this layout only.
• Reuse factor about 1.78 nodes per slot.
• The brief's 5-slot sample uses unknown coordinates, so 5 and 9 are not comparable. Frame length depends on the layout.
• 16 unit tests pass.
Notes: Output of python tdma_scheduler.py --demo. Proven optimal for this layout only. The brief shows a 5-slot sample with unknown coordinates, so 5 and 9 cannot be compared.

## Slide 6
EMANE integration, the bridge
6
TDMA Schedule Optimizer and EMANE Integration
[run]
schedule.json
Part 1 output
emane_bridge.py
converts matrix
schedule XML + pathloss.eel
validated against the schema
EMANE 1.5.3
16 radios
traffic + analyze
measure delivery
• emane_bridge.py converts the Part 1 matrix into an EMANE TDMA schedule event (XML) and a pathloss topology (pathloss.eel).
• Schedule XML validates against EMANE's tdmaschedule.xsd and round-trips back to the exact matrix.
• Node_NN name maps to NEM id NN.
Notes: The bridge turns the matrix into an EMANE schedule event and a pathloss file. Each radio runs in its own network namespace in the emulation.

## Slide 7
Radio values and why
7
TDMA Schedule Optimizer and EMANE Integration
1 ms slots, 10 microsecond overhead (covers 500 m flight time).
[from docs, not run]
2.4 GHz, 10 MHz bandwidth, 9 Mbps. Noise floor -100 dBm is computed.
Power: the schedule XML sets 20 dBm but the PHY log showed 0 dBm. The applied power is unresolved.
[run] for the logs
Computed SNR for a clean link: 26 dB at 20 dBm, 6 dB at 0 dBm. Both give 100 percent on the 9 Mbps curve.
Computed, not measured
The 500 m range is enforced by the 200 dB pathloss for out-of-range pairs, not by a receiver sensitivity setting.
[run] for the EEL contents
Notes: Slot length and overhead come from the brief and the EMANE guide. Power is unresolved: the XML sets 20 dBm but the PHY log showed 0 dBm. The SNR figures are computed, not measured.

## Slide 8
Experiments and the three variants
8
TDMA Schedule Optimizer and EMANE Integration
part1
The real schedule, expected to deliver with no collisions. [from docs, not run]
distance1 (control)
1-hop only, should bring back hidden-terminal loss.
allslot0 (control)
Everyone in slot 0, receivers should hear nothing.
Metrics [run]
Per-pair packet delivery ratio, EMANE accept and drop tables, scheduler.scheduleAcceptFull, the ScheduleInfoTable per NEM.
Notes: Each control is expected to fail. A passing part1 only means something next to controls that fail.

## Slide 9
Live run results (EMANE v1.5.3, saved run)
9
TDMA Schedule Optimizer and EMANE Integration
[run]
Variant | Slots | Clean-link delivery | Blocked-pair delivery | SINR drop counter
part1 | 9 | 99.5 % | none exist | 0 bytes
distance1 | 4 | 98.4 % | 0.1 % (64 pairs) | 39,182,660 bytes
allslot0 | 9 | none exist | 0.0 % (84 pairs) | 0 bytes
• 20 s per variant at 500 packets per second per radio. Not re-run in the final verification.
• All 16 radios installed their schedules, scheduleAcceptFull = 1 everywhere.
• part1: clean links delivered 99.5 percent, 240 of 240 pairs agreed with the schedule. The SINR drop counter read 0 bytes. "0 measured collisions" means that counter and nothing broader.
• distance1 control: clean links delivered 98.4 percent, close to part1, so delivery alone does not separate the variants. The SINR drop counter showed 39,182,660 bytes dropped, and 64 hidden-terminal pairs delivered 0.1 percent.
• allslot0 control: 0 percent delivery. This shows half-duplex blocking, not interference.
• Bugs found and fixed to get here: CRLF in pathloss.eel aborting the event service, the receiver frequency mismatch (suspected cause, not isolated) and the build-essential and tee issues in the Docker build.
Notes: Numbers are from the saved earlier run in results/. They were not re-run in the final verification. distance1 clean-link delivery is close to part1, so the SINR counter is the main evidence of collisions.

## Slide 10
Limitations and honesty
10
TDMA Schedule Optimizer and EMANE Integration
• Minimum slots proven optimal only for this 16-node layout, not in general.
• Unit-disk model: no fading, no partial-quality links, range is a hard cliff by design.
• Static topology, no node movement.
• Applied transmit power not resolved. No 499 m pair run live. The nearest out-of-range pair run live was 600 m.
• Clearly separate what was measured from what is reasoned from documentation.
Notes: Be direct about what was measured and what was reasoned.

## Slide 11
What to do next
11
TDMA Schedule Optimizer and EMANE Integration
[from docs, not run]
• Resolve the applied transmit power and rerun.
• Measured runs across more topologies and node counts.
• Mobility and a distance-based pathloss model with capture effects.
• Multi-frequency schedules for more reuse.
Notes: Future work, none of it done.